## Slide 1
BUFFER R
_en
SYNC REG FILE
L
R
D
_MR
CP
rdL_addr
rdR_addr
wr_addr
_rdL_en
_rdR_en
_wr_en
RAM
D
A[15:0]
Attach RAM /ROM to
R Bus so they can
participate in ALU
as other side from
the other registers
Or UART.
ALU
L
R
Result
ALU L Bus
ALU R Bus
ALU Result Bus
Address Bus Hi [15:8]
Address Bus Lo [7:0]
Address Bus
BUFFER I
_en
RAM isolation from result bus to avoid read / write or RAM leaking between Result Bus and R Bus.
Buffer I _oe = _wr
Buffer R _oe = _RAM _oe
Register file is a general
purpose register set
BUFFER AH
_en
BUFFER AL
_en
BUFFER R
_en
D[7:0]
D[15:8]
D[24:16]
CONTROL LOGIC
_wr
_oe
C
Z
O
GT
LT
EQ
NE
CONTROL LOGIC
FLAGS
C
Z
O
GT
LT
EQ
NE
CP
_en
BUFFER L
_en`
_cin
TBD: Flags Reg
write _en may only be enabled for specific ops
Optional : Flags reg on L Bus means we can store it
to RAM or to another reg and do arbitrary bitwise comparisons on the result.
Optional: But if we also allow it to be restored from RAM or a REG or ROM then that
might be extra useful – eg to set or clear carry before arithmetic.
Or is Carry a special case? Perhaps on a sophisticated CPU
stashing the flags might be useful, but here?
Address Bus [15:0]
Optional extras: a presettable auto-counting MAR?
Or a settable address register that autoincrements after each read will save time on copy operations; otherwise multiple instructions required for increment, with carry to MARHI. Basically a second program counter like thing.
And I have no dedicted stack pointer either.
ROM
A D[7:0]
_oe
_oe=_addrmode_immediate
rom_addrbushi_buf
rom_addrbuslo_buf
UART
D
BUFFER L
_en
BUFFER I
_en
UART Buffer isolation needed to prevent writes and reads from UART on one bus leaking over to the other bus.
Buffer I _oe = wr Buffer L _oe = _rd (wr is +ve edge latch)
wr
_rd
CONTROL LOGIC
_txe
_rxf
uart_lbus_buf
uart_alubus_buf
ram_alubus_buf
ram_rbus_buf
rom_rbus_buf
MARLO
Q
MARHI
Q
D
_en
CP
PCHI
Q
D
_en
CP
D
count_en
_pe
CP
BUFFER R
_en
BUFFER R
_en
PCLO
Q
D
count_en
_pe
CP
BUFFER AH
_en
BUFFER AL
_en
BUFFER L
_en
BUFFER L
_en
BUFFER L
_en
BUFFER L
_en
BUFFER AH
_en
BUFFER AL
_en
MAR primary function is Address Bus index.
Optionally MAR can join either/both L Bus or R Bus depending
on flexibility desired.
So MAR also acts as a GP register on both ALUinput busses.
PCHI/LO Primary function is Address Bus index.
Optionally PC can join either/both L Bus or R Bus depending on whether I want to permit PC arithmetic.
Here PC is shown outputting to
L Bus.
PCHITmp
Q
D
_en
CP
_MR
_MR
_oe=_addrmode_pc
_oe=_addrmode_register
marhi_addrbushi_buf
marlo_addrbuslo_buf
marhi_lbus_buf
marhi_rbus_buf
marlo_lbus_buf
marhi_rbus_buf
pchi_lbus_buf
pclo_lbus_buf
pchi_addrbushi_buf
pclo_addrbuslo_buf
GS100 bus stripx2 $3.45 https://www.globalspecialties.com/solderless-breadboards/breadboards-bus-strips/item/34-gs-100.html
£3.28 https://www.mouser.co.uk/ProductDetail/Global-Specialties/GS-100?qs=uv8bPZ39CeNa73a0uSX5Lw%3D%3D
BB100R is the busboard equiv
£2.70 https://www.digikey.co.uk/product-detail/en/global-specialties/GS-100/BKGS-100-ND/5231302
74als576 – inverting dtype – oe + clk + bus layout 74HC7292 clock divider 4> 2billion – good for clock speed control off a fast crystal or for a freq counter - https://uk.rs-online.com/web/p/clock-dividers/5400461/
FIX NAMES IMMEDIATE/DIRECT/REGISTER
CONTROL LOGIC EASIER IF ALL DEVICES CAN WRITE TO RBUS OR LBUS AS DON’T NEED TO FORCE L AND R JUST ONE OR THE OTHER
IReg Lo _en
D[7:0]
BUFFER R
_en
instreg_rbus_buf
D[48:8]
+ve edge Registers but could be latches if the output of the ALU is a register
USE 40 pin ribbon and connector for busses?
20 pin for connector + 4x10 pin for chips = 60
Remaining 3 pins for caps? Or spacing?? Very tight.
So instead use the approach in the
DONE!!
!!!! DON’T SET FLAGS WHEN OPERATION IS A JUMP (IE SETTING THOSE REG) AS IT MAKES
“IF NFLAG & CFLAG” logic impossible
!!! CANT WORK UNLESS FIX BECAUSE SETTING PCHITMP CLEARS THE CONDITION SO WE NEVER CONDITIONALLY JUMP
Initially only allow devs to just write to LBUS?
If I postpone being able to write
to more than one bus then I don’t
need to wire in the Buffers to separate busses and can just use the devices own _OE pin.
And simpler still if initially don’t permit read of MAR/PC
on LBUS at all.
But these options mean a lot of rewiring
when adding buffers.
Use unused op 2 or 3 for that?
If not enough bit space then do X=X+5 so targ is fixed to src OR only permit lower 16 ALU ops HMM Bad for logic ops.
OR only allow 3 bits for src and/or targ so we can only do that with GP registers ??
Targ fixed to src is probably ok for many logical ops??
Direct
addressing
buffer
Immediate
addressing
buffer
Instruction Reg
for low byte
ROM
A[15:0]
D[48:8]
_oe
Raw {PCHI, PCLO}
Address Bus
multiplexes {PCHI, PCLO}
{MARHI, MARLO}
{DIRECTHI, DIRECTLO}
Horizontal Encoded “WIDE ROM” Design
PC [15:0]
DIRECTHI
DIRECTLO
PCHI
MARLO
PCLO
MARHI
This design doesn’t permit
X=Y+KONST  or worse perhaps
X = X logicialOp KONST FIXED

## Slide 2
BUFFER R
_en
SYNC REG FILE
L
R
D
_MR
CP
rdL_addr
rdR_addr
wr_addr
_rdL_en
_rdR_en
_wr_en
RAM
D
ROM
D[15:0]
A[15:0]
A[15:0]
Attach RAM /ROM to
R Bus so they can
participate in ALU
as other side from
the other registers
Or UART.
ALU
L
R
Result
ALU L Bus
ALU R Bus
ALU Result Bus
Address Bus Hi / 8
Address Bus Lo / 8
A/16
BUFFER I
_en
RAM isolation from result bus to avoid read / write or RAM leaking between Result Bus and R Bus.
Buffer I _oe = _wr
Buffer R _oe = _RAM _oe
Register file is a general
purpose register set
BUFFER AH
_en
BUFFER AL
_en
BUFFER R
_en
D[7:0]
D[7:0]
D[15:8]
D[23:16]
CONTROL LOGIC
_wr
_oe
C
Z
O
GT
LT
EQ
NE
CONTROL LOGIC
FLAGS
C
Z
O
GT
LT
EQ
NE
CP
_en
BUFFER L
_en`
_cin
TBD: Flags Reg
write _en may only be enabled for specific ops
Optional : Flags reg on L Bus means we can store it
to RAM or to another reg and do arbitrary bitwise comparisons on the result.
Optional: But if we also allow it to be restored from RAM or a REG or ROM then that
might be extra useful – eg to set or clear carry before arithmetic.
Or is Carry a special case? Perhaps on a sophisticated CPU
stashing the flags might be useful, but here?
Address Bus (A/16)
A/16
Optional extras: a presettable auto-counting MAR?
_oe
_oe=_addrmode_immediate
rom_addrbushi_buf
rom_addrbuslo_buf
UART
D
BUFFER L
_en
BUFFER I
_en
UART Buffer isolation needed to prevent writes and reads from UART on one bus leaking over to the other bus.
Buffer I _oe = wr Buffer L _oe = _rd (wr is +ve edge latch)
wr
_rd
CONTROL LOGIC
_txe
_rxf
uart_lbus_buf
uart_alubus_buf
ram_alubus_buf
ram_rbus_buf
rom_rbus_buf
MARLO
Q
MARHI
Q
D
_en
CP
PCHI
Q
D
_en
CP
D
count_en
_pe
CP
BUFFER R
_en
BUFFER R
_en
PCLO
Q
D
count_en
_pe
CP
BUFFER AH
_en
BUFFER AL
_en
BUFFER L
_en
BUFFER L
_en
BUFFER L
_en
BUFFER L
_en
BUFFER AH
_en
BUFFER AL
_en
MAR primary function is Address Bus index.
Optionally MAR can join either/both L Bus or R Bus depending
on flexibility desired.
So MAR also acts as a GP register on both ALUinput busses.
PCHI/LO Primary function is Address Bus index.
Optionally PC can join either/both L Bus or R Bus depending on whether I want to permit PC arithmetic.
Here PC is shown outputting to
L Bus.
PCHITmp
Q
D
_en
CP
_MR
_MR
_oe=_addrmode_pc
_oe=_addrmode_register
marhi_addrbushi_buf
marlo_addrbuslo_buf
marhi_lbus_buf
marhi_rbus_buf
marlo_lbus_buf
marhi_rbus_buf
pchi_lbus_buf
pclo_lbus_buf
pchi_addrbushi_buf
pclo_addrbuslo_buf
GS100 bus stripx2 $3.45 https://www.globalspecialties.com/solderless-breadboards/breadboards-bus-strips/item/34-gs-100.html
£3.28 https://www.mouser.co.uk/ProductDetail/Global-Specialties/GS-100?qs=uv8bPZ39CeNa73a0uSX5Lw%3D%3D
BB100R is the busboard equiv
£2.70 https://www.digikey.co.uk/product-detail/en/global-specialties/GS-100/BKGS-100-ND/5231302
74als576 – inverting dtype – oe + clk + bus layout 74HC7292 clock divider 4> 2billion – good for clock speed control off a fast crystal or for a freq counter - https://uk.rs-online.com/web/p/clock-dividers/5400461/
FIX NAMES IMMEDIATE/DIRECT/REGISTER
CONTROL LOGIC EASIER IF ALL DEVICES CAN WRITE TO RBUS OR LBUS AS DON’T NEED TO FORCE L AND R JUST ONE OR THE OTHER
IReg Hi
_en
IReg Mid
_en
IReg Lo _en
D[7:0]
BUFFER R
_en
instreg_rbus_buf
D[15:8]
D[23:16]
Latches
+ve edge Registers but could be latches if the output of the ALU is a register
USE 40 pin ribbon and connector for busses?
20 pin for connector + 4x10 pin for chips = 60
Remaining 3 pins for caps? Or spacing?? Very tight.
So instead use the approach in the
!!!! DON’T SET FLAGS WHEN OPERATION IS A JUMP (IE SETTING THOSE REG) AS IT MAKES
“IF NFLAG & CFLAG” logic impossible
!!! CANT WORK UNLESS FIX BECAUSE SETTING PCHITMP CLEARS THE CONDITION SO WE NEVER CONDITIONALLY JUMP
If I postpone being able to write
to more than one bus then I don’t
need to wire in the Buffer L/R devices.
Eg if the reg’s write to L and ROM/RAM to R
Then I think that’s a simplification especially
If PC and MAR can’t be read via ALU
This design doesn’t permit
X=Y+KONST  or worse perhaps
X = X logicialOp KONST FIXED
Use unused op 2 or 3 for that?
If not enough bit space then do X=X+5 so targ is fixed to src OR only permit lower 16 ALU ops HMM Bad for logic ops.
OR only allow 3 bits for src and/or targ so we can only do that with GP registers ??
Targ fixed to src is probably ok for many logical ops??

## Slide 3
BUFFER R
_en
SYNC REG FILE
L
R
D
_MR
CP
rdL_addr
rdR_addr
wr_addr
_rdL_en
_rdR_en
_wr_en
MARLO
Q
MARHI
Q
D
_en
CP
PCHI
Q
D
_en
CP
D
count_en
_pe
CP
BUFFER R
_en
BUFFER R
_en
PCLO
Q
D
count_en
_pe
CP
BUFFER AH
_en
BUFFER AL
_en
BUFFER L
_en
BUFFER L
_en
BUFFER L
_en
BUFFER L
_en
UART
D
BUFFER L
_en
RAM
D
ROM
D[15:0]
A[15:0]
A[15:0]
BUFFER AH
_en
BUFFER AL
_en
MAR primary function is Address Bus index.
Optionally MAR can join either/both L Bus or R Bus depending
on flexibility desired.
So MAR also acts as a GP register on both ALUinput busses.
PCHI/LO Primary function is Address Bus index.
Optionally PC can join either/both L Bus or R Bus depending on whether I want to permit PC arithmetic.
Here PC is shown outputting to
L Bus.
Attach RAM /ROM to
R Bus so they can
participate in ALU
as other side from
the other registers
Or UART.
ALU
L
R
Result
ALU L Bus
ALU R Bus
ALU Result Bus
Address Bus Hi / 8
Address Bus Lo / 8
Address Bus (A/16)
A/16
PCHITmp
Q
D
_en
CP
BUFFER I
_en
BUFFER I
_en
UART Buffer isolation needed to prevent writes and reads from UART on one bus leaking over to the other bus.
Buffer I _oe = wr Buffer L _oe = _rd (wr is +ve edge latch)
RAM isolation from result bus to avoid read / write or RAM leaking between Result Bus and R Bus.
Buffer I _oe = _wr
Buffer R _oe = _RAM _oe
Register file is a general
purpose register set
_MR
_MR
BUFFER AH
_en
BUFFER AL
_en
BUFFER R
_en
D[7:0]
D[7:0]
D[15:8]
D[23:16]
CONTROL LOGIC
wr
_rd
_wr
_oe
CONTROL LOGIC
C
Z
O
N
GT
LT
EQ
NE
CONTROL LOGIC
FLAGS
C
Z
O
N
GT
LT
EQ
NE
CP
_en
BUFFER L
_en`
_cin
TBD: Flags Reg
write _en may only be enabled for specific ops
Optional : Flags reg on L Bus means we can store it
to RAM or to another reg and do arbitrary bitwise comparisons on the result.
Optional: But if we also allow it to be restored from RAM or a REG or ROM then that
might be extra useful – eg to set or clear carry before arithmetic.
Or is Carry a special case? Perhaps on a sophisticated CPU
stashing the flags might be useful, but here?
_txe
_rxf
A/16
Optional extras: a presettable auto-counting MAR?
_oe
_addrmode_immediate
_addrmode_pc
_addrmode_register
Must be tristate register
to save a chip
rom_addrbushi_buf
rom_addrbuslo_buf
marhi_addrbushi_buf
marlo_addrbuslo_buf
marhi_lbus_buf
marhi_rbus_buf
marlo_lbus_buf
marhi_rbus_buf
pchi_lbus_buf
pclo_lbus_buf
uart_lbus_buf
uart_alubus_buf
ram_alubus_buf
ram_rbus_buf
rom_rbus_buf
pchi_addrbushi_buf
pclo_addrbuslo_buf
GS100 bus stripx2 $3.45 https://www.globalspecialties.com/solderless-breadboards/breadboards-bus-strips/item/34-gs-100.html
£3.28 https://www.mouser.co.uk/ProductDetail/Global-Specialties/GS-100?qs=uv8bPZ39CeNa73a0uSX5Lw%3D%3D
BB100R is the busboard equiv
£2.70 https://www.digikey.co.uk/product-detail/en/global-specialties/GS-100/BKGS-100-ND/5231302

## Slide 4
BUFFER R
_en
SYNC REG FILE
L
R
D
_MR
CP
rdL_addr
rdR_addr
wr_addr
_rdL_en
_rdR_en
_wr_en
MARLO
Q
MARHI
Q
D
_en
CP
PCHI
Q
D
_en
CP
D
count_en
_pe
CP
BUFFER R
_en
BUFFER R
_en
PCLO
Q
D
count_en
_pe
CP
BUFFER AH
_en
BUFFER AL
_en
BUFFER L
_en
BUFFER L
_en
BUFFER L
_en
BUFFER L
_en
UART
D
BUFFER L
_en
RAM
D
ROM
D[15:0]
A[15:0]
A[15:0]
BUFFER AH
_en
BUFFER AL
_en
MAR primary function is Address Bus index.
Optionally MAR can join either/both L Bus or R Bus depending
on flexibility desired.
So MAR also acts as a GP register on both ALUinput busses.
PCHI/LO Primary function is Address Bus index.
Optionally PC can join either/both L Bus or R Bus depending on whether I want to permit PC arithmetic.
Here PC is shown outputting to
L Bus.
Attach RAM /ROM to
R Bus so they can
participate in ALU
as other side from
the other registers
Or UART.
ALU
L
R
Result
ALU L Bus
ALU R Bus
ALU Result Bus
Address Bus Hi / 8
Address Bus Lo / 8
Address Bus (A/16)
A/16
PCHITmp
Q
D
_en
CP
BUFFER I
_en
BUFFER I
_en
UART Buffer isolation needed to prevent writes and reads from UART on one bus leaking over to the other bus.
Buffer I _oe = wr Buffer L _oe = _rd (wr is +ve edge latch)
RAM isolation from result bus to avoid read / write or RAM leaking between Result Bus and R Bus.
Buffer I _oe = _wr
Buffer R _oe = _RAM _oe
Register file is a general
purpose register set
_MR
_MR
BUFFER AH
_en
BUFFER AL
_en
BUFFER R
_en
D[7:0]
D[7:0]
D[15:8]
D[23:16]
CONTROL LOGIC
wr
_rd
_wr
_oe
CONTROL LOGIC
C
Z
O
GT
LT
EQ
NE
CONTROL LOGIC
FLAGS
C
Z
O
GT
LT
EQ
NE
CP
_en
BUFFER L
_en`
_cin
TBD: Flags Reg
write _en may only be enabled for specific ops
Optional : Flags reg on L Bus means we can store it
to RAM or to another reg and do arbitrary bitwise comparisons on the result.
Optional: But if we also allow it to be restored from RAM or a REG or ROM then that
might be extra useful – eg to set or clear carry before arithmetic.
Or is Carry a special case? Perhaps on a sophisticated CPU
stashing the flags might be useful, but here?
_txe
_rxf
A/16
Optional extras: a presettable autocounting MAR?
_oe

## Slide 5
BUFFER O
SYNC REG FILE
L
R
D
_MR
CP
rdL_addr
rdR_addr
wr_addr
_rdL_en
_rdR_en
_wr_en
MARLO
Q
MARHI
Q
D
_en
CP
PCHI
Q
D
_en
CP
D
count_en
_pe
CP
BUFFER
BUFFER
PCLO
Q
D
count_en
_pe
CP
BUFFER
BUFFER
BUFFER
BUFFER
BUFFER
BUFFER
UART
D
BUFFER O
RAM
D
ROM
D[15:0]
A
A
BUFFER
BUFFER
MAR can join either L Bus or R Bus or both or neither bus depending
on flexibility desired.
Here MAR is a GP
register on both ALU
input busses but has additional
Address Bus function
PC can join L Bus or R Bus or neither bus depending on whether I want to permit PC arithmetic in addition to its primary Address Bus function.
Here PC only outputs to
L Bus.
Attach RAM /ROM to
R Bus so they can
participate in ALU
as other side from
the other registers
Or UART.
ALU
L
R
Result
ALU L Bus
ALU R Bus
ALU Result Bus
Address Bus Hi
Address Bus Lo
Address Bus (A/16)
A/16
PCHITmp
Q
D
_en
CP
BUFFER I
BUFFER I
Buffer isolation needed to prevent writes and reads from UART on one bus leaking over to the other bus.
Buffer I _oe = wr Buffer O _oe = _rd (wr is +ve edge latch)
RAM isolation from result bus to avoid read / write or RAM leaking between Result Bus and R Bus.
Buffer I _oe = _wr
Buffer O _oe = _RAM _oe
Register file is a general
purpose register set
_MR
_MR
BUFFER
BUFFER
BUFFER
D[7:0]
D[7:0]
D[15:8]
D[23:16]
CONTROL LOGIC
_txe
_rxf
wr
_rd
_wr
_oe
CONTROL LOGIC
CONTROL LOGIC
FLAGS
C
Z
O
GT
LT
EQ
NE
C
Z
O
GT
LT
EQ
NE
CP

## Slide 6
REG in
Flags In
same as ALU out
N bit ALU select
?5 Muxed with C?
X
Y
ALU
BUF
ALU out
BUS
ROM
AL/AH
D
ROM out
PCLO
D
RAM
AL/AH
D
RAM out
RAM in
MARLO in
UART
D
UART in
DISPLAY
DEVICE
D
CU
Carry, Zero , Equals, Overflow
flags
FLAGS
C, Z, E
[control lines out]
Op code
flags
Program Counter & ROM
Control Logic
Register File
and ALU
RAM
Output device
Control line in
Data
Flags
Data – tri-state buffer
Not enough control bits for ALU – only 2 but 3 or 4 really needed + 1 for the carry in.
Also ought to be able to clear flags register, or at least clear carry perhaps?
Cant add/sub/logic Immediate
Cant do Add/Sub with and without observing the carry.
2 ALU bits, 3 bits out ctl (#7 is unused), 3 bits in ctl.
Also Warren suggested making the DISP bidirectional – see the UART.
And only got 2 general purpose registers – 3 or 4 much more flexible.
No signed arithmetic and no overflow.
Low ROM byte wasted for all but Immediate access – can byte be used for control lines otherwise?
Control line out
UART out
Useless instructions in decoder??
Cannot carry program in RAM – do I want program in RAM?
PC incrementer requires an 8 bit adder probably – cos PC is 8 bits and this will only get worse if we go to 16 bits address - and the +1 input to added probably has to be the same width. So switch adder/mux circuit for an 8 or 16 bit loadable counter (8 bits hi and 8 bits lo PC like CSC but how does PC work in CSCvon8?). Still need a line for PC-in though.
Since “Flags in” = “ALU out” we cannot set flags without emitting ALU to bus. So can’t set flags using a compare instruction with an immediate or with a value from RAM or anywhere else. FlagsIn=ALUout was done to preserve flags during non ALU operations. << unless mux ROM/RAM into the alu inputsnote
MARLO
OE D C
MARHI
C D OE
MARHI in
PCHI
D
PCHI
TMP
D
PCLO in
PCHi in
PCHITmp in
ADAPTED TO 16 BIT ADDRESS AND MORE GP REGISTERS
IN ready
OUT ready
(4) REG Y addr
(4)REG X addr
D
X
Y
Carry in
JMP $1234
PCHIin=En PCHI _TMP = ROMOUT = 12
JMPin=En PCLO = ROMOUT = 34 PCHI=PCHI_TMP=12
JCS $1234
PCHIin=En PCHI _TMP =BUS = 12
IF-CS JMPin=En PCLO = BUS = 34 PCHI=PCHI_TMP=12
ROM Three x AT28C256-15PU = 96k ROM addressed as 15 bits
RAMZP
ZP BUF
RAMZP
ROM
data
To support zero page addressing -
0 pulldown resistors effective when MARHI OE is disabled
D OE
RAMZP
Both MAR use 74574
74 547 uses CP (no WE) so system CP is gated by an enable line
74244 buffer
ROM
data
Each PC =
2x74HC163
Vs
2x74HCT193
??
Reset
Reset
SN74HCT74N
Needed for MR
circuit

## Slide 7
ZP BUF
REG in
Flags In
same as ALU out
N bit ALU select
?5 Muxed with C?
Y
X
ALU
BUF
ALU out
BUS
ROM
AL/AH
D
ROM out
PCLO
D
RAM
AL/AH
D
RAM out
RAM in
MARLO in
UART
D
UART in
DISPLAY
DEVICE
D
CU
Carry, Zero , Equals, Overflow
flags
FLAGS
C, Z, E
[control lines out]
Op code
flags
Program Counter & ROM
Control Logic
Register File
and ALU
RAM
Output device
UART out
MARLO
OE D C
MARHI
C D OE
MARHI in
PCHI
D
PCHI
TMP
D
JMP in
JMP in
PCHI in
IN ready
OUT ready
(4) REG Y addr
(4)REG X addr
D in
Y
X
Carry in
RAMZP
RAMZP
To support zero page addressing -
0 pulldown resistors effective when MARHI OE is disabled
D OE
RAMZP
Both MAR use 74574
74 547 uses CP (no WE) so system CP is gated by an enable line
74244 buffer
ROM
LOW8
Ov
Pull
BUF
D
BUF
D

## Slide 8
REG in
(2) REG W addr
Flags In
same as ALU out
N bit ALU select
?5 Muxed with C?
L
R
ALU
BUF
ALU out
BUS
ROM
AL/AH
D
ROM out
PCLO
D
RAM
AL/AH
D
RAM out
RAM in
MARLO in
UART
D
UART in
DISPLAY
DEVICE
D
CU
Carry, Zero , Equals, Overflow
flags
FLAGS
C, Z, E
[control lines out]
Op code
flags
Program Counter & ROM
Control Logic
Register File
and ALU
RAM
Output device
Control line in
Data
Flags
Data – tri-state buffer
Not enough control bits for ALU – only 2 but 3 or 4 really needed + 1 for the carry in.
Also ought to be able to clear flags register, or at least clear carry perhaps?
Cant add/sub/logic Immediate
Cant do Add/Sub with and without observing the carry.
2 ALU bits, 3 bits out ctl (#7 is unused), 3 bits in ctl.
Also Warren suggested making the DISP bidirectional – see the UART.
And only got 2 general purpose registers – 3 or 4 much more flexible.
No signed arithmetic and no overflow.
Low ROM byte wasted for all but Immediate access – can byte be used for control lines otherwise?
Control line out
UART out
Useless instructions in decoder??
Cannot carry program in RAM – do I want program in RAM?
PC incrementer requires an 8 bit adder probably – cos PC is 8 bits and this will only get worse if we go to 16 bits address - and the +1 input to added probably has to be the same width. So switch adder/mux circuit for an 8 or 16 bit loadable counter (8 bits hi and 8 bits lo PC like CSC but how does PC work in CSCvon8?). Still need a line for PC-in though.
Since “Flags in” = “ALU out” we cannot set flags without emitting ALU to bus. So can’t set flags using a compare instruction with an immediate or with a value from RAM or anywhere else. FlagsIn=ALUout was done to preserve flags during non ALU operations. << unless mux ROM/RAM into the alu inputsnote
MARLO
OE D C
MARHI
C D OE
MARHI in
PCHI
D
PCHI
TMP
D
JMP in
JMP in
PCHI in
ADAPTED TO 16 BIT ADDRESS AND MORE GP REGISTERS
IN ready
OUT ready
(2) REG R addr
(2)REG L addr
D
L
R
Carry in
JMP $1234
PCHIin=En PCHI _TMP = ROMOUT = 12
JMPin=En PCLO = ROMOUT = 34 PCHI=PCHI_TMP=12
JCS $1234
PCHIin=En PCHI _TMP =BUS = 12
IF-CS JMPin=En PCLO = BUS = 34 PCHI=PCHI_TMP=12
ROM Three x AT28C256-15PU = 96k ROM addressed as 15 bits
RAMZP
ZP BUF
RAMZP
ROM
data
To support zero page addressing -
0 pulldown resistors effective when MARHI OE is disabled
D OE
RAMZP
Both MAR use 74574
74 547 uses CP (no WE) so system CP is gated by an enable line
74244 buffer
ROM
data

## Slide 9
A in
B in
Flags in
= ALU out
2 bit ALU select
A
B
1
0
ALU
BUF
ALU out
BUS
PC
PC out
BUF
ROM
D
A
D
ROM out
ADD1
D
D+1
PC in
RAM
A
D
RAM out
RAM in
MAR
D
MAR in
DISP
REG
D
DISP in
DISPLAY
DEVICE
D
MAR out
BUF
CU
Carry, Zero , Equals
C & Z & E
FLAGS
C, Z, E
[control lines]
Op code
C & Z & E
Program Counter
Control Logic
[tri-state]
ROM
Registers and ALU
RAM
Output device
Out control line
Data
Other control line
Data – tri-state buffer
BUF
B out
BUF
A out
Not enough control bits for ALU – only 2 but 3 or 4 really needed + 1 for the carry in.
Also ought to be able to clear flags register, or at least clear carry perhaps?
Cant add/sub/logic Immediate
Cant do Add/Sub with and without observing the carry.
2 ALU bits, 3 bits out ctl (#7 is unused), 3 bits in ctl.
Also Warren suggested making the DISP bidirectional – see the UART.
And only got 2 general purpose registers – 3 or 4 much more flexible.
No signed arithmetic and no overflow.
Low ROM byte wasted for all but Immediate access – can byte be used for control lines otherwise?
In control line
DISP out
Useless instructions in decoder??
Cannot carry program in RAM – do I want program in RAM?
PC incrementer requires an 8 bit adder probably – cos PC is 8 bits and this will only get worse if we go to 16 bits - and the +1 input probably has to be the same width. So switch adder/mux circuit for an 8 or 16 bit loadable counter (8 bits hi and 8 bits lo PC like CSC but how does PC work in CSCvon8?). Still need a line for PC-in though.
Since Flags in = ALU out we cannot set flags without emitting ALU to bus. So can’t set flags using a compare instruction with an immediate or with a value from RAM or anywhere else. FlagsIn=ALUout was done to preserve flags during non ALU operations.
Need more control lines meaning only use low rom for immediate values when required and rest of time use low rom as control lines

## Slide 10
REG in
(2) REG W addr
Flags in
= ALU out
N bit ALU select
?5 Muxed with C?
L
R
1
ALU
BUF
ALU out
BUS
ROM
A (16)
D
ROM out
PCLO
D
RAM
A(16)
D
RAM out
RAM in
MARLO in
UART
D
UART in
DISPLAY
DEVICE
D
CU
Carry, Zero , Equals
C & Z & E
FLAGS
C, Z, E
[control lines out]
Op code
C & Z & E
Program Counter & ROM
Control Logic
Register File
and ALU
RAM
Output device
Control line in
Data
Flags
Data – tri-state buffer
Not enough control bits for ALU – only 2 but 3 or 4 really needed + 1 for the carry in.
Also ought to be able to clear flags register, or at least clear carry perhaps?
Cant add/sub/logic Immediate
Cant do Add/Sub with and without observing the carry.
2 ALU bits, 3 bits out ctl (#7 is unused), 3 bits in ctl.
Also Warren suggested making the DISP bidirectional – see the UART.
And only got 2 general purpose registers – 3 or 4 much more flexible.
No signed arithmetic and no overflow.
Low ROM byte wasted for all but Immediate access – can byte be used for control lines otherwise?
Control line out
UART out
Useless instructions in decoder??
Cannot carry program in RAM – do I want program in RAM?
PC incrementer requires an 8 bit adder probably – cos PC is 8 bits and this will only get worse if we go to 16 bits address - and the +1 input to added probably has to be the same width. So switch adder/mux circuit for an 8 or 16 bit loadable counter (8 bits hi and 8 bits lo PC like CSC but how does PC work in CSCvon8?). Still need a line for PC-in though.
Since “Flags in” = “ALU out” we cannot set flags without emitting ALU to bus. So can’t set flags using a compare instruction with an immediate or with a value from RAM or anywhere else. FlagsIn=ALUout was done to preserve flags during non ALU operations.
MARLO
D
MARHI
D
MARHI in
PCHI
D
PCHI
TMP
D
PCLO in
PCHI in
PCHI TMP in
ADAPTED TO 16 BIT ADDRESS AND MORE GP REGISTERS
IN ready
OUT ready
(2) REG R addr
(2)REG L addr
D
L
R
Carry in

## Slide 11
A in
B in
Flags in
= ALU out
2 bit ALU select
0 : A+B
1 : A-B
2 : PASS A
3 : PASS B
A
B
1
0
ALU
BUF
ALU out
BUS
PC
PC out
BUF
ROM
D
A
D
ROM out
ADD1
D
D+1
PC in
RAM
A
D
RAM out
RAM in
MAR
D
MAR in
DISP
REG
D
DISP in
DISPLAY
DEVICE
D
MAR out
BUF
CU
Carry, Zero , Equals
C & Z & E
FLAGS
C, Z, E
[control lines]
Op code
C & Z & E
Program Counter
Control Logic
[tri-state]
ROM
Registers and ALU
RAM
Output device
Out control line
Data
Other control line
Data – tri-state buffer
Not enough control bits for ALU – only 2 but 3 or 4 really needed + 1 for the carry in.
Also ought to be able to clear flags register, or at least clear carry perhaps?
Cant add/sub/logic Immediate
Cant do Add/Sub with and without observing the carry.
2 ALU bits, 3 bits out ctl (#7 is unused), 3 bits in ctl.
Also Warren suggested making the DISP bidirectional – see the UART.
And only got 2 general purpose registers – 3 or 4 much more flexible.
No signed arithmetic and no overflow.
Low ROM byte wasted for all but Immediate access – can byte be used for control lines otherwise?
In control line
DISP out
Useless instructions in decoder??
Cannot carry program in RAM – do I want program in RAM?
PC incrementer requires an 8 bit adder probably – cos PC is 8 bits and this will only get worse if we go to 16 bits address - and the +1 input to added probably has to be the same width. So switch adder/mux circuit for an 8 or 16 bit loadable counter (8 bits hi and 8 bits lo PC like CSC but how does PC work in CSCvon8?). Still need a line for PC-in though.
Since Flags in = ALU out we cannot set flags without emitting ALU to bus. So can’t set flags using a compare instruction with an immediate or with a value from RAM or anywhere else. FlagsIn=ALUout was done to preserve flags during non ALU operations.
Need more control lines meaning only use low rom for immediate values when required and rest of time use low rom as control lines
ADDR HI
D
ADDR LO
D
Needed for 16 bit address

## Slide 12
A in
B in
Flags in
2 bit ALU select
A
B
1
0
ALU
BUF
ALU out
BUS
PC
PC out
BUF
ROM
D
A
D
ROM out
ADD1
D
D+1
PC in
RAM
A
D
RAM out
RAM in
MAR
D
MAR in
DISP
REG
D
DISP in
DISPLAY
DEVICE
D
MAR out
BUF
CU
Carry, Zero , Equals
C & Z & E
FLAGS
C, Z, E
[control lines]
Op code
C & Z & E
Program Counter
Control Logic
[tri-state]
ROM
Registers and ALU
RAM
Output device
Out control line
Data
Other control line
Data – tri-state buffer
BUF
B out
BUF
A out
Inefficient use of control lines around register and ALU.
2 ALU bits, 3 bits out ctl (#7 is unused), 3 bits in ctl.
If we take #7 out plus Aout and Bout lines away
In control line

## Slide 13
D
2 bit ALU select
1
0
ALU
BUF
ALU out
BUS
A in
B in
PC
PC out
BUF
ROM
D
A
D
ROM out
ADD1
D
D+1
PC in
A
B
RAM
A
D
RAM out
RAM in
MAR
D
MAR in
DISP
REG
D
DISP in
DISPLAY
DEVICE
D
MAR out
BUF
CU
Carry, Zero , Equals
C & Z & E
FLAGS
C, Z, E
[control lines]
Op code
C & Z & E
Flags in
Program Counter
Control Logic
[tri-state]
ROM
Registers and ALU
RAM
Output device
In/Out control line
Data
Other control line
Data – tri-state buffer
C

## Slide 14
ALU sel
(4 + M & C)
A
B
1
0
ALU
BUF
ALU out
BUS
A in
B in
PC
PC out
BUF
ROM
D
A
D
ROM out
ADD1
D
D+1
PC in
RAM
A
D
RAM out
RAM in
MAR
D
MAR in
DISP
REG
D
DISP in
DISPLAY
DEVICE
D
Could we take a lines from the ram and other components straight into the ALU via a MUX and avoid the bus?
Can I support an update in place with arbitrary registers
RegX = ALU(Reg Y, Reg Z)
Can I add immediate to a reg without having the added value from the rom go via a reg? Ie “ADD RA, 10” add 10 to RA without overwriting RB
Might need to introduce an instruction register to hold the immediate value “10” to do that??
Mux: Support immediate arith (without loading reg)
Mux:Support relative jumps
Mux: Support walking memory locations
MAR out
BUF
CU
Carry, Zero ( Negative, Overflow,
Magnitude?? )
C & Z
FLAGS
C & Z
[All other control]
Op code
C & Z
Flags in
Program Counter
Control Logic

## Slide 15
2 bit ALU select
A
B
1
0
ALU
BUF
ALU out
BUS
A in
B in
PC
PC out
BUF
ROM
D
A
D
ROM out
ADD1
D
D+1
PC in
RAM
A
D
RAM out
RAM in
MAR
D
MAR in
DISP
REG
D
DISP in
DISPLAY
DEVICE
D
Could we take a lines from the ram and other components straight into the ALU via a MUX and avoid the bus?
Can I add immediate to a reg without having the added value from the rom go via a reg? Ie “ADD RA, 10” add 10 to RA without overwriting RB
Might need to introduce an instruction register to hold the immediate value “10” to do that or mux the ROM data into the ALU.
Mux: Support immediate arith (without loading reg)
Mux:Support relative jumps
Mux: Support walking memory locations
MAR out
BUF
CU
Carry, Zero , Equals
C & Z & E
FLAGS
C, Z, E
[control lines]
Op code
C & Z & E
Flags in
Program Counter
Control Logic
[tri-state]
ROM
Registers and ALU
RAM
Output device