## Slide 1
REG in
(2) REG W addr
Flags In
same as ALU out
N bit ALU select
?5 Muxed with C?
L
R
ALU
BUF
ALU out
BUS
ROM
AL/AH
D
ROM out
PCLO
D
RAM
AL/AH
D
RAM out
RAM in
MARLO in
UART
D
UART in
DISPLAY
DEVICE
D
CU
Carry, Zero , Equals, Overflow
flags
FLAGS
C, Z, E
[control lines out]
Op code
flags
Program Counter & ROM
Control Logic
Register File
and ALU
RAM
Output device
Control line in
Data
Flags
Data – tri-state buffer
Not enough control bits for ALU – only 2 but 3 or 4 really needed + 1 for the carry in.
Also ought to be able to clear flags register, or at least clear carry perhaps?
Cant add/sub/logic Immediate
Cant do Add/Sub with and without observing the carry.
2 ALU bits, 3 bits out ctl (#7 is unused), 3 bits in ctl.
Also Warren suggested making the DISP bidirectional – see the UART.
And only got 2 general purpose registers – 3 or 4 much more flexible.
No signed arithmetic and no overflow.
Low ROM byte wasted for all but Immediate access – can byte be used for control lines otherwise?
Control line out
UART out
Useless instructions in decoder??
Cannot carry program in RAM – do I want program in RAM?
PC incrementer requires an 8 bit adder probably – cos PC is 8 bits and this will only get worse if we go to 16 bits address - and the +1 input to added probably has to be the same width. So switch adder/mux circuit for an 8 or 16 bit loadable counter (8 bits hi and 8 bits lo PC like CSC but how does PC work in CSCvon8?). Still need a line for PC-in though.
Since “Flags in” = “ALU out” we cannot set flags without emitting ALU to bus. So can’t set flags using a compare instruction with an immediate or with a value from RAM or anywhere else. FlagsIn=ALUout was done to preserve flags during non ALU operations. << unless mux ROM/RAM into the alu inputsnote
MARLO
OE D C
MARHI
C D OE
MARHI in
PCHI
D
PCHI
TMP
D
JMP in
JMP in
PCHI in
ADAPTED TO 16 BIT ADDRESS AND MORE GP REGISTERS
IN ready
OUT ready
(2) REG R addr
(2)REG L addr
D
L
R
Carry in
JMP $1234
PCHIin=En PCHI _TMP = ROMOUT = 12
JMPin=En PCLO = ROMOUT = 34 PCHI=PCHI_TMP=12
JCS $1234
PCHIin=En PCHI _TMP =BUS = 12
IF-CS JMPin=En PCLO = BUS = 34 PCHI=PCHI_TMP=12
ROM Three x AT28C256-15PU = 96k ROM addressed as 15 bits
RAMZP
ZP BUF
RAMZP
ROM
data
To support zero page addressing -
0 pulldown resistors effective when MARHI OE is disabled
D OE
RAMZP
Both MAR use 74574
74 547 uses CP (no WE) so system CP is gated by an enable line
74244 buffer
ROM
data

## Slide 2
A in
B in
Flags in
= ALU out
2 bit ALU select
A
B
1
0
ALU
BUF
ALU out
BUS
PC
PC out
BUF
ROM
D
A
D
ROM out
ADD1
D
D+1
PC in
RAM
A
D
RAM out
RAM in
MAR
D
MAR in
DISP
REG
D
DISP in
DISPLAY
DEVICE
D
MAR out
BUF
CU
Carry, Zero , Equals
C & Z & E
FLAGS
C, Z, E
[control lines]
Op code
C & Z & E
Program Counter
Control Logic
[tri-state]
ROM
Registers and ALU
RAM
Output device
Out control line
Data
Other control line
Data – tri-state buffer
BUF
B out
BUF
A out
Not enough control bits for ALU – only 2 but 3 or 4 really needed + 1 for the carry in.
Also ought to be able to clear flags register, or at least clear carry perhaps?
Cant add/sub/logic Immediate
Cant do Add/Sub with and without observing the carry.
2 ALU bits, 3 bits out ctl (#7 is unused), 3 bits in ctl.
Also Warren suggested making the DISP bidirectional – see the UART.
And only got 2 general purpose registers – 3 or 4 much more flexible.
No signed arithmetic and no overflow.
Low ROM byte wasted for all but Immediate access – can byte be used for control lines otherwise?
In control line
DISP out
Useless instructions in decoder??
Cannot carry program in RAM – do I want program in RAM?
PC incrementer requires an 8 bit adder probably – cos PC is 8 bits and this will only get worse if we go to 16 bits - and the +1 input probably has to be the same width. So switch adder/mux circuit for an 8 or 16 bit loadable counter (8 bits hi and 8 bits lo PC like CSC but how does PC work in CSCvon8?). Still need a line for PC-in though.
Since Flags in = ALU out we cannot set flags without emitting ALU to bus. So can’t set flags using a compare instruction with an immediate or with a value from RAM or anywhere else. FlagsIn=ALUout was done to preserve flags during non ALU operations.
Need more control lines meaning only use low rom for immediate values when required and rest of time use low rom as control lines

## Slide 3
REG in
(2) REG W addr
Flags in
= ALU out
N bit ALU select
?5 Muxed with C?
L
R
1
ALU
BUF
ALU out
BUS
ROM
A (16)
D
ROM out
PCLO
D
RAM
A(16)
D
RAM out
RAM in
MARLO in
UART
D
UART in
DISPLAY
DEVICE
D
CU
Carry, Zero , Equals
C & Z & E
FLAGS
C, Z, E
[control lines out]
Op code
C & Z & E
Program Counter & ROM
Control Logic
Register File
and ALU
RAM
Output device
Control line in
Data
Flags
Data – tri-state buffer
Not enough control bits for ALU – only 2 but 3 or 4 really needed + 1 for the carry in.
Also ought to be able to clear flags register, or at least clear carry perhaps?
Cant add/sub/logic Immediate
Cant do Add/Sub with and without observing the carry.
2 ALU bits, 3 bits out ctl (#7 is unused), 3 bits in ctl.
Also Warren suggested making the DISP bidirectional – see the UART.
And only got 2 general purpose registers – 3 or 4 much more flexible.
No signed arithmetic and no overflow.
Low ROM byte wasted for all but Immediate access – can byte be used for control lines otherwise?
Control line out
UART out
Useless instructions in decoder??
Cannot carry program in RAM – do I want program in RAM?
PC incrementer requires an 8 bit adder probably – cos PC is 8 bits and this will only get worse if we go to 16 bits address - and the +1 input to added probably has to be the same width. So switch adder/mux circuit for an 8 or 16 bit loadable counter (8 bits hi and 8 bits lo PC like CSC but how does PC work in CSCvon8?). Still need a line for PC-in though.
Since “Flags in” = “ALU out” we cannot set flags without emitting ALU to bus. So can’t set flags using a compare instruction with an immediate or with a value from RAM or anywhere else. FlagsIn=ALUout was done to preserve flags during non ALU operations.
MARLO
D
MARHI
D
MARHI in
PCHI
D
PCHI
TMP
D
PCLO in
PCHI in
PCHI TMP in
ADAPTED TO 16 BIT ADDRESS AND MORE GP REGISTERS
IN ready
OUT ready
(2) REG R addr
(2)REG L addr
D
L
R
Carry in

## Slide 4
A in
B in
Flags in
= ALU out
2 bit ALU select
0 : A+B
1 : A-B
2 : PASS A
3 : PASS B
A
B
1
0
ALU
BUF
ALU out
BUS
PC
PC out
BUF
ROM
D
A
D
ROM out
ADD1
D
D+1
PC in
RAM
A
D
RAM out
RAM in
MAR
D
MAR in
DISP
REG
D
DISP in
DISPLAY
DEVICE
D
MAR out
BUF
CU
Carry, Zero , Equals
C & Z & E
FLAGS
C, Z, E
[control lines]
Op code
C & Z & E
Program Counter
Control Logic
[tri-state]
ROM
Registers and ALU
RAM
Output device
Out control line
Data
Other control line
Data – tri-state buffer
Not enough control bits for ALU – only 2 but 3 or 4 really needed + 1 for the carry in.
Also ought to be able to clear flags register, or at least clear carry perhaps?
Cant add/sub/logic Immediate
Cant do Add/Sub with and without observing the carry.
2 ALU bits, 3 bits out ctl (#7 is unused), 3 bits in ctl.
Also Warren suggested making the DISP bidirectional – see the UART.
And only got 2 general purpose registers – 3 or 4 much more flexible.
No signed arithmetic and no overflow.
Low ROM byte wasted for all but Immediate access – can byte be used for control lines otherwise?
In control line
DISP out
Useless instructions in decoder??
Cannot carry program in RAM – do I want program in RAM?
PC incrementer requires an 8 bit adder probably – cos PC is 8 bits and this will only get worse if we go to 16 bits address - and the +1 input to added probably has to be the same width. So switch adder/mux circuit for an 8 or 16 bit loadable counter (8 bits hi and 8 bits lo PC like CSC but how does PC work in CSCvon8?). Still need a line for PC-in though.
Since Flags in = ALU out we cannot set flags without emitting ALU to bus. So can’t set flags using a compare instruction with an immediate or with a value from RAM or anywhere else. FlagsIn=ALUout was done to preserve flags during non ALU operations.
Need more control lines meaning only use low rom for immediate values when required and rest of time use low rom as control lines
ADDR HI
D
ADDR LO
D
Needed for 16 bit address

## Slide 5
A in
B in
Flags in
2 bit ALU select
A
B
1
0
ALU
BUF
ALU out
BUS
PC
PC out
BUF
ROM
D
A
D
ROM out
ADD1
D
D+1
PC in
RAM
A
D
RAM out
RAM in
MAR
D
MAR in
DISP
REG
D
DISP in
DISPLAY
DEVICE
D
MAR out
BUF
CU
Carry, Zero , Equals
C & Z & E
FLAGS
C, Z, E
[control lines]
Op code
C & Z & E
Program Counter
Control Logic
[tri-state]
ROM
Registers and ALU
RAM
Output device
Out control line
Data
Other control line
Data – tri-state buffer
BUF
B out
BUF
A out
Inefficient use of control lines around register and ALU.
2 ALU bits, 3 bits out ctl (#7 is unused), 3 bits in ctl.
If we take #7 out plus Aout and Bout lines away
In control line

## Slide 6
D
2 bit ALU select
1
0
ALU
BUF
ALU out
BUS
A in
B in
PC
PC out
BUF
ROM
D
A
D
ROM out
ADD1
D
D+1
PC in
A
B
RAM
A
D
RAM out
RAM in
MAR
D
MAR in
DISP
REG
D
DISP in
DISPLAY
DEVICE
D
MAR out
BUF
CU
Carry, Zero , Equals
C & Z & E
FLAGS
C, Z, E
[control lines]
Op code
C & Z & E
Flags in
Program Counter
Control Logic
[tri-state]
ROM
Registers and ALU
RAM
Output device
In/Out control line
Data
Other control line
Data – tri-state buffer
C

## Slide 7
ALU sel
(4 + M & C)
A
B
1
0
ALU
BUF
ALU out
BUS
A in
B in
PC
PC out
BUF
ROM
D
A
D
ROM out
ADD1
D
D+1
PC in
RAM
A
D
RAM out
RAM in
MAR
D
MAR in
DISP
REG
D
DISP in
DISPLAY
DEVICE
D
Could we take a lines from the ram and other components straight into the ALU via a MUX and avoid the bus?
Can I support an update in place with arbitrary registers
RegX = ALU(Reg Y, Reg Z)
Can I add immediate to a reg without having the added value from the rom go via a reg? Ie “ADD RA, 10” add 10 to RA without overwriting RB
Might need to introduce an instruction register to hold the immediate value “10” to do that??
Mux: Support immediate arith (without loading reg)
Mux:Support relative jumps
Mux: Support walking memory locations
MAR out
BUF
CU
Carry, Zero ( Negative, Overflow,
Magnitude?? )
C & Z
FLAGS
C & Z
[All other control]
Op code
C & Z
Flags in
Program Counter
Control Logic

## Slide 8
2 bit ALU select
A
B
1
0
ALU
BUF
ALU out
BUS
A in
B in
PC
PC out
BUF
ROM
D
A
D
ROM out
ADD1
D
D+1
PC in
RAM
A
D
RAM out
RAM in
MAR
D
MAR in
DISP
REG
D
DISP in
DISPLAY
DEVICE
D
Could we take a lines from the ram and other components straight into the ALU via a MUX and avoid the bus?
Can I add immediate to a reg without having the added value from the rom go via a reg? Ie “ADD RA, 10” add 10 to RA without overwriting RB
Might need to introduce an instruction register to hold the immediate value “10” to do that or mux the ROM data into the ALU.
Mux: Support immediate arith (without loading reg)
Mux:Support relative jumps
Mux: Support walking memory locations
MAR out
BUF
CU
Carry, Zero , Equals
C & Z & E
FLAGS
C, Z, E
[control lines]
Op code
C & Z & E
Flags in
Program Counter
Control Logic
[tri-state]
ROM
Registers and ALU
RAM
Output device